## Slide 1
ME2 — Voice Controlled Smart Device
Always-on keyword + intent recognition at the edge · no cloud round-trip
2 October 2026 · [author / team] · Model · Dataset · Training on an RTX 5060 laptop GPU · Validation on RPi 4
Model
Mic · 16 kHz → log-mel 64 × 498
Conformer encoder × 4 · 64-dim · 3-seed ensemble
one 5 s window after the wake word (not streaming, no KV-cache)
Intent head (19 + OOS)
Slot heads (6 × 3)
Actuator
Raspberry Pi 4
Item | Value
Parameters / weights | 0.88 M · 4.46 MB fp32 (2.78 MB int8)
Validation on the Raspberry Pi 4
Item | Value
Keyword / intent acc | 48.0 % / 46.9 % (97.9 % once woken)
False-accept rate | 0.0 % (0 of 10 out-of-scope)
Latency p95 / RTF | 1,657 ms e2e (model 101 ms) / 0.020
Runtime | onnxruntime · 2 thr
First live holdout run, laptop speaker → Pi mic (196 + 10 trials). Every miss was a missed wake word; wake model v2 is being retrained and re-run.
Dataset
Item | Value
Source | HF airimonda/ai231-me2-voice-commands
Hours / utts | 8.74 h / 15,378 (+1,250 synth. negatives)
Speakers | 428 IDs, disjoint train / test / holdout
Labels | 19 intents (+ OOS) · 6 slots × 3 values
Group recordings + Common Voice, SLURP, FSC, SNIPS, Speech Commands, TimersAndSuch; 78 % of train is synthetic speech.
Training on the A100 cluster
Item | Value
Cluster | no A100: 1× RTX 5060 Laptop GPU (8 GB)
Objective | CE (intent + masked slot) + misfire term
Optimiser | AdamW · lr 3e-3 · cosine · batch 64
Steps / loss | 7,905 / 1.66 (seed 0, best epoch 51)
p. 1 / 2

## Slide 2
To Be Submitted
GitHub repository | github.com/airimonda/vcm-me2 — public, MIT
Dataset location | huggingface.co/datasets/airimonda/ai231-me2-voice-commands (public, no DOI yet)
A100 cluster | none: 1× RTX 5060 Laptop GPU · ~12–13 min per seed · seeds 0, 1, 2
Model weights | tag v1.0 in the repo (models/*.onnx, models/ckpt/*.pt) — MIT
What the reviewer will look for
# | Item | Status
1 | Repo public, one-command reproduction | Partial: public; commands in docs/paper.md §10
2 | Dataset licensed and citable (DOI) | To do: no licence or DOI yet
3 | Training logs + final checkpoint committed | Done: results/runs/, models/ckpt/
4 | Pi 4 latency reproduced by the posted script | Done: scripts/bench_onnx.py
5 | Held-out test set, unseen speakers | Done: 0 speakers shared
6 | Baseline of comparable size compared | Done: DS-CNN M 0.861 vs 0.935
p. 2 / 2